## Slide 1: EADAS
Abhimanyu Chopra – G00885635 Lalitha baskharuni – G00949261 Nisarg patel – G00944795 Sammy lin – G00429253

## Slide 2: Problem statement
In person monitoring of the elderly is not always convenient.
Solution : EADAS – Elderly Asset Distress Alarm System
  Monitors
    Orientation & acceleration to detect fall
    Heart rate to detect spike or fall
    Location, in case the elderly doesn’t respond
  Alert
    Sends status/location and time as sms to a set mobile number

## Slide 3: Hardware block diagram
MSP-430EXPFR6989
Pulse Sensor
Gyro
Keypad
GSM/GPS Module
LCD
Power Supply
GSM Power Supply
Key:
Input
Output
Power
Logic

## Slide 4: Software flow diagram Initialization Sequence
Initialize Clock
Initialize SPI
Initialize UART
Initialize Timer
Initialize ADC
Initialize LCD
Initialize Gyro
Start
Request Phone Number
Initialize FONA

## Slide 5: Software flow diagram Application
Read Gyro
Get GPS Coordinates & Time
Read Heart Rate
Print to LCD
DISTRESS?
Send SMS
No
Yes

## Slide 6: Sms Alert Example

## Slide 7: Software tools
Code Composer Studio v6.1 – IDE for TI microcontrollers
Git – Source code management
Kicad – Schematic design
SketchUp – 3D design
Open source frameworks & components
  Arduino C++ Libraries ported to Ti Launchpad in C (Gyro)
  Implementation approach – pulsesensor.com (Pulse sensor)

## Slide 8: Project timeline
A long time ago, in a galaxy
far, far away…

## Slide 9: Project timeline
12/8/2015
12/1/2015
11/24/2015
Demo!
Complete pulse/SMS code
11/17/2015
11/10/2015
11/03/2015
10/27/2015
10/20/2015
10/13/2015
10/06/2015
09/29/2015
09/22/2015
09/15/2015
09/08/2015
Formed team
EADAS is born!
Hardware researched/sourced
Hardware received and distributed
Complete documentation & 3D printing
Distributed tasks amongst team
Started code
Gyro working
UART comm working/keypad working/PCB cut/complete assembly
Pulse sensor working
LCD code working
09/01/2015

## Slide 10: EADAS Case Design

## Slide 11: Issues/solution
SPI interface – Hard to initially understand and get configuration right on Launchpad
Timing issues – printf to CCS console caused timing issues and UART/Timer/ADC stopped working as expected
Pulse Sensor – A very finicky sensor. Took a lot of time to troubleshoot errors
Integration – Required lots of testing and code changes
Most components purchased from Sparkfun/Adafruit come with Arduino libraries. Took full advantage and ported to MSP430 C/C++
ISRs – They had to be really fast
Didn't include buzzard in PCB design
3D Printing – Takes a lot of time

## Slide 12: Demo Time!

## Slide 13: Questions?

## Slide 14: Motd