EADAS
Abhimanyu Chopra
Lalitha Baskharuni
Nisarg Patel
Sammy Lin

---
Project Objectives
In person monitoring of the elderly is not always convenient
Solution :
EADAS- Elderly Asset Distress Alarm System

---
Block diagram
Pulse Sensor
LCD
MSP-430EXPFR6989
Gyro
GSM/GPS Module
Keypad
GSM Power Supply
Power Supply
Key:
Input
Output
Power
Logic

---
Box & Lid

---
System Flow Chart
Start
Capture phone number
Initialize FONA
Initialize clock
Initialize clock
Read gyro
Initialize SPI
Check heart rate
Initialize UART
Distress?
Initialize timer
No
Yes
Get GPS location
Initialize ADC
Send SMS
Initialize LCD
Print to LCD
Initialize gyro

---
Project Time-line

---
Project Time-line
LCD code working
UART comm working/keypad working/PCB cut/complete assembly
Pulse sensor working
Gyro working
Started code
Distributed tasks amongst team
Complete documentation & 3D printing
Hardware received and distributed
Hardware researched/sourced
Complete pulse/SMS code
EADAS is born!
Formed team
Demo!
12/8/2015
12/1/2015
11/24/2015
11/17/2015
11/10/2015
11/03/2015
10/27/2015
10/20/2015
10/13/2015
10/06/2015
09/29/2015
09/22/2015
09/15/2015
09/08/2015
09/01/2015

---
Software
Code Composer Studio v6.1 – Integrated development environment for TI microcontrollers
Git – Source code control
Arduino C++ libraries ported to TI Launchpad in C (for gyro)

---
Issues/Solutions
SPI interface – Hard to initially understand and get configuration right on Launchpad
UART – printf to CCS console caused timing issues and UART wasn't working as expected
Most components purchased from Sparkfun/Adafruit come with Arduino libraries. Took full advantage and ported to MSP430 C/C++
ISRs – They had to be really fast
Didn't include buzzard in PCB design

---
Demo Time!

---
Questions?

---
MotD